## Slide 1
Proba
A High-Performance, Low-Traffic Probabilistic
Spatial Memory Streaming Prefetcher
Yinting Huang · Jacky Wong · Sam Ainsworth
Huawei Newton Research Centre · Imperial College London · University of Edinburgh

## Slide 2
L1$
Notes: SMS prefetcher has also made its way to production core. Arm Neoverse V2, which powers systems including NVIDIA Grace and AWS Graviton4, uses SMS at both cache levels: SMS at L1 and global SMS at L2. SMS is able to work alongside other prefetchers in the cache hierarchy like stride, best offset and correlated miss cache because it captures spatial access patterns that other predictors can miss. It makes a distinct contribution to the processor’s ability to bring data in before it is needed. Therefore, improving SMS has practical relevance for the commercial architecture.

## Slide 3
L1$
Stride
Page
SMS
SIP
Notes: SMS prefetcher has also made its way to production core. Arm Neoverse V2, which powers systems including NVIDIA Grace and AWS Graviton4, uses SMS at both cache levels: SMS at L1 and global SMS at L2. SMS is able to work alongside other prefetchers in the cache hierarchy like stride, best offset and correlated miss cache because it captures spatial access patterns that other predictors can miss. It makes a distinct contribution to the processor’s ability to bring data in before it is needed. Therefore, improving SMS has practical relevance for the commercial architecture.

## Slide 4
L1$
Stride
Page
SMS
SIP
L1PRQ
Notes: SMS prefetcher has also made its way to production core. Arm Neoverse V2, which powers systems including NVIDIA Grace and AWS Graviton4, uses SMS at both cache levels: SMS at L1 and global SMS at L2. SMS is able to work alongside other prefetchers in the cache hierarchy like stride, best offset and correlated miss cache because it captures spatial access patterns that other predictors can miss. It makes a distinct contribution to the processor’s ability to bring data in before it is needed. Therefore, improving SMS has practical relevance for the commercial architecture.

## Slide 5
Spatial Memory Streaming is Important
SMS
GSMS (Global)
Arm Neoverse V2
- NVIDIA Grace
- AWS Graviton4
L1$
Stride
Page
SMS
SIP
L1PRQ
L2$
CMC
BO
GSMS
TBW
L2PRQ
Notes: SMS prefetcher has also made its way to production core. Arm Neoverse V2, which powers systems including NVIDIA Grace and AWS Graviton4, uses SMS at both cache levels: SMS at L1 and global SMS at L2. SMS is able to work alongside other prefetchers in the cache hierarchy like stride, best offset and correlated miss cache because it captures spatial access patterns that other predictors can miss. It makes a distinct contribution to the processor’s ability to bring data in before it is needed. Therefore, improving SMS has practical relevance for the commercial architecture.

## Slide 6
First access identifies the context
First eviction completes the training
Trigger PC1
Eviction
PC1:
Prefetch
B+1 B+3 B+5 B+7 B+8 B+9 B+11 B+12 B+13
+1
+2
+3
+4
SMS: exploiting spatial correlation across fix-sized regions
Region A
+5
+6
+7
+8
+9
+10
+11
+12
+13
+14
+15
+16
PC1:
+1
+2
+3
+4
Trigger PC1
Region B
+5
+6
+7
+8
+9
+10
+11
+12
+13
+14
+15
+16

## Slide 7
Problem: What pattern should the prefetcher remember?
Same Trigger Context
Stored Pattern
New Observation
Replace?

## Slide 8
Same Trigger Context
Stored Pattern
New Observation
Replace?
Problem: What pattern should the prefetcher remember?

## Slide 9
Same Trigger Context
Stored Pattern
New Observation
Replace?
Problem: What pattern should the prefetcher remember?

## Slide 10
Same Trigger Context
Stored Pattern
New Observation
Replace?
Problem: What pattern should the prefetcher remember?

## Slide 11
Same Trigger Context
Stored Pattern
New Observation
Limitation: Simple replacement discards all historical behaviour…
Replace?
Can we do better?
Problem: What pattern should the prefetcher remember?

## Slide 12
Genetic Algorithms: “Survival of the Fittest”
What we want:
We want a storage-efficient representation for these patterns.
We want to remove bad patterns overtime.
We want to keep good patterns overtime.
If patterns appear frequently enough
Those are the patterns worth remembering
Using a Probabilistic Approach!
Problem: What pattern should the prefetcher remember?

## Slide 13
Core Idea: Probabilistic Pattern Update
Treat the update of a stored pattern with a new observation as a stochastic process.
Store only a single bit pattern per entry.
New Observation
Stored Pattern
Updated Pattern
STEP 1: INTERSECTION

## Slide 14
New Observation
Stored Pattern
Updated Pattern
STEP 2: Probabilistic Insertion
Insertion Probability p
Core Idea: Probabilistic Pattern Update
Treat the update of a stored pattern with a new observation as a stochastic process.
Store only a single bit pattern per entry.

## Slide 15
New Observation
Stored Pattern
Updated Pattern
STEP 3: Probabilistic Deletion
Deletion Probability q
Core Idea: Probabilistic Pattern Update
Treat the update of a stored pattern with a new observation as a stochastic process.
Store only a single bit pattern per entry.
How do we control p and q (to control aggression)?

## Slide 16
New Observation
Stored Pattern
AND
OR
Limitation:
(Since it is not probabilistic) You need to store two patterns!
Only support two aggression modes, limiting fine-grain control.
Maintain two patterns: accuracy-biased and coverage-biased.
Issue one pattern based on current bandwidth utilization.
Prior Methods: Dual Spatial Pattern Prefetcher (DSPatch)
Updated Patterns
Can we do better?

## Slide 17
Accuracy Seeking
Coverage Seeking
Accuracy Feedback Decides How Aggressive Proba Should Be
Dynamic Decision-making
Accuracy
Yes
No
State --
State ++
< Threshold
State | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Insertion Probability (p) | 0.01 | 0.05 | 0.10 | 0.40 | 1.00 | 1.00 | 1.00 | 1.00
Deletion Probability (q) | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 0.60 | 0.40 | 0.20

## Slide 18
Proba uses multiple trigger contexts to improve coverage
Overlapping contexts can lead to overprediction.
New Observation
PC 0x1234
Offset 7
Absolute
Accuracy
100%
75%
Marginal
Accuracy
100%
0%
The offset context adds only one new incorrect prediction
Marginal Accuracy: What is the best context to use?

## Slide 19
Evaluated on ChampSim.
Baseline: Stride prefetcher at L1.
Evaluated SMS-based prefetchers:
Run at L2 cache
Track 4 KiB spatial regions
Use an iso-storage budget of roughly 10 KiB
Code and Artifact available @ GitHub!
Evaluation

## Slide 20
Proba delivers a 6.6% geomean speedup with only 8.5% additional DRAM traffic.
SPECspeed 2017: Speedup and DRAM Traffic
Higher is Better ⟶
⟵ Lower is Better

## Slide 21
Proba achieves the highest overall prefetch accuracy.
LLC coverage can be lower for workloads that are poorly suited to SMS.
SPECspeed 2017: Accuracy and Coverage
Higher is Better ⟶
Higher is Better ⟶

## Slide 22
Proba’s advantage is more evident as contention rises.
On CloudSuite, Proba achieves a 7.9% geomean speedup, nearly twice the nearest contender Gaze.
4-Core CloudSuite: Speedup and DRAM Traffic
Higher is Better ⟶
⟵ Lower is Better

## Slide 23
For More: Read Our Paper!
More Benchmarks
DRAM Sensitivity
Homogeneous Multicore
Ablation Study
And More!

## Slide 24
We Present Proba: a practical SMS-based prefetcher for next-gen processor.
Probabilistic updates provide a powerful alternative to storage-heavy counters and dual-pattern schemes.
Update probabilities control how quickly the prefetcher learns and forgets.
Accuracy feedback adjusts aggression level with fine-grain control.
Marginal accuracy assesses the unique contribution of overlapping contexts.
More questions? Contact: yh653@cam.ac.uk
Takeaways

## Slide 25
Proba
Design Overview

## Slide 26
Evaluation
Single Core Performance Analysis

## Slide 27
Evaluation
Performance vs. Bandwidth

## Slide 28
Evaluation
Multi-Prefetcher Stack

## Slide 29
Evaluation
Ablation Study